## Slide 1
The Consequences of Plate Geometry on Plasma Activated Media*
Soheila Mohades, Amanda M. Lietz, Juliusz Kruszelnicki and Mark J. Kushner
University of Michigan
Ann Arbor, MI 48109-2122 USA
smohades@umich.edu
International Conference on Plasma Medicine
June 2018
ICPM_2018
* Work supported by National Science Foundation and Department of Energy Office of Fusion Energy Science
Notes: 1

## Slide 2
AGENDA
Plasma Activation of Liquids in Well Plates
Model Description: nonPDPSIM
Flow with Plate Geometry
RONS in Gas and Liquid phase
Multipulse Effects on RONS
Concluding Remarks
ICPM_2018
University of Michigan
Institute for Plasma Science & Engr.
Notes: 2

## Slide 3
ATMOSPHERIC PRESSURE PLASMA JETS
Atmospheric Pressure Plasma Jets (APPJs) are used in plasma medicine in several modes:
  Direct treatment of cells and tissues.
  Activation of liquid for plasma activation of media (PAM).
APPJ operation with rare gas (helium or argon) having small air impurities generates reactive oxygen and nitrogen species (RONS).
Solvation or transport of gas phase species into liquid and chemical reactions in liquid are two pathways of RONS generation in liquid phase.
ICPM_2018
University of Michigan
Institute for Plasma Science & Engr.
K. Tominami, et al. Japn. J. Appl. Phys. 55. 01AF03 (2016).
Notes: 3

## Slide 4
TREATMENT OF LIQUID IN WELL PLATES
Plasma activation of liquids in biological studies is often conducted with a well plate.
The characteristics of the well plate and height of the plate wall can affect gas dynamics, mixture, and discharge above the liquid:
  Large surface/ volume plate: petri dishes or 6-well plate
  Small surface/ volume plates: Eppendorf tube or 96-well plate
  In this talk I will discuss results from computational investigation on the effect of well plate geometry on gas flow and RONS production.
ICPM_2018
University of Michigan
Institute for Plasma Science & Engr.
Joh, H. et al. Applied Phys. Letters, 5, 101 (2012)
 Joseph-Marie Plewa et al 2014 New J Phys. 16 043027
Notes: 4

## Slide 5
Radiation Transport
Plasma Hydrodynamics
Poisson’s Equation
Gas Phase Plasma
Bulk Electron Energy
Transport
Kinetic “Beam”
Electron Transport
Neutral Transport
Navier-Stokes
Neutral and Plasma
Chemistry
Liquid Phase Plasma
2-D unstructured mesh
Time slicing algorithms between plasma and fluid timescales.
Poisson’s equation is solved throughout the computational domain during voltage pulse.
Diffusion into/out of liquid limited by Henry’s law equilibrium at the surface.
Liquid evaporates into gas with vapor pressure source.
Neutral plasma during afterglow.
MODEL: nonPDPSIM
ICPM_2018
University of Michigan
Institute for Plasma Science & Engr.

## Slide 6
Radiation Transport
Plasma Hydrodynamics
Poisson’s Equation
Gas Phase Plasma
Bulk Electron Energy
Transport
Kinetic “Beam”
Electron Transport
Neutral Transport
Navier-Stokes
Neutral and Plasma
Chemistry
Liquid Phase Plasma
2-D unstructured mesh
Time slicing algorithms between plasma and fluid timescales.
Poisson’s equation is solved throughout the computational domain during voltage pulse.
Diffusion into/out of liquid limited by Henry’s law equilibrium at the surface.
Liquid evaporates into gas with vapor pressure source.
Neutral plasma during afterglow.
MODEL: nonPDPSIM
ICPM_2018
University of Michigan
Institute for Plasma Science & Engr.
Notes: 6
6

## Slide 7
Liquid plasma is treated identically to gas as a partially ionized substance.
Surface tension is addressed by specifying species able to pass through vapor/liquid interface.
  Neutrals: Diffusion across interface is limited by Henry’s law equilibrium at the surface layer.
  Ions and photons: All enter into liquid.
Liquid evaporates into gas with source given by its vapor pressure.
Liquid
Evaporation
Dissolved
gases
Ions, Photons
Solvated
Henry's Law
Low h: density in water saturates (O3aq, N2Oaq, H2aq)
High h: solvation depletes gas (H2O2aq, HO2NO2aq,)
nonPDPSIM: TREATMENT OF LIQUID
ICPM_2018
University of Michigan
Institute for Plasma Science & Engr.
Notes: 7
Liquid plasma is treated identically to gas as a partially ionized substance with Higher density and Specified permittivity
Surface tension is addressed by specifying species able to pass through vapor/liquid interface.
Diffusion into water is limited by Henry’s law equilibrium at the surface layer.
Solvated species “stay in liquid”, cannot go back to gas phase.
Liquid evaporates into gas with source given by its vapor pressure.

## Slide 8
HE PLASMA JET SCHEMATIC
+30 kV (350 ns) on top electrode, grounded bottom electrode
Alumina reactor tube, 1 mm nozzle radius
1 cm between nozzle tip to 3 mm water in dielectric plate
Rim height: 0 to 5 mm
Feed gas: He = 99.97% + O2/N2 (63/237 ppm), 4 slm
Humid ambient air (O2/N2/H2O = 79.5/20/0.5), 1 atm
Liquid: H2O + 8 ppm O2aq
ICPM_2018
S. Mohades, M. Laroussi, V. Maruthamuthu, J. Phys. D 50, 285205 (2017)
University of Michigan
Institute for Plasma Science & Engr.
Notes: 8
cylindrically symmetric

## Slide 9
POT +30kV Se 1×1022 ne 5×1014 cm-3s-1 cm-3
GAS FLOW AND DISCHARGE: BASE CASE
Steady-state flow established before plasma initiated.
+30 kV, 350 ns pulse width; 370 ns animated
Discharge initiates in electrodes gap and propagates through nozzle
~ 1.5 mm plate rim
ICPM_2018
He
N2
H2O
2.6 ×1019 2×1019 5.8×1018 5×1018 cm-3
O2
Animation Slide
University of Michigan
Institute for Plasma Science & Engr.
(linear)
(4-dec)
(4-dec)
2-dec
Notes: 9
ADD ANIMATION

## Slide 10
GAS DYNAMICS
Geometry of plate changes the gas composition above liquid.
High rim produces stagnation above liquid. Low rim produces cross flow over liquid.
Higher He density and water vapor in high rim plate while gas density of N2 and O2 is lower above the liquid.
Feed gas: He = 99.97% + O2/N2 (63/237 ppm), 4 slm
2-dec
High rim
Flat rim
2.4 ×1019 2×1019 5.8×1017 5×1018 cm-3
He
N2
H2O
O2
ICPM_2018
University of Michigan
Institute for Plasma Science & Engr.
2.6 ×1019 2×1019 5.8×1018 5×1018 cm-3
Notes: 10

## Slide 11
POT +30kV Se 1×1022 cm-3s-1 ne 5×1014 cm-3
MIN MAX
Log scale
University of Michigan
Institute for Plasma Science & Engr.
Animation Slide
+30 kV, 350 ns, 370 ns animated
Flush (flat) rim
He plume is surrounded by air as in a conventional APPJ.
Ionization wave is confined to He, and propagates across water layer.
IW speed lower than with high rim.
JET INTERACTING WITH FLAT RIM PLATE
ICPM_2018
Notes: Not v2

## Slide 12
MIN MAX
Log scale
University of Michigan
Institute for Plasma Science & Engr.
Animation Slide
+30 kV, 350 ns, 360 ns animated
~5 mm plate rim
Well is largely filled with He – lacks confinement of He plume by air.
Ionization wave spreads volumetrically above the liquid in He rich environment
POT +30kV Se 1×1022 cm-3s-1 ne 5×1014 cm-3
JET INTERACTING WITH HIGH RIM PLATE
ICPM_2018
Notes: Humidity:

## Slide 13
Densities of O and O3 above liquid are both higher for flat and low rim due to proximity (and diffusion) of O2 into ionization wave.
O3 production depends on O density in high ambient of O2.
Densities (cm-3, 3-dec) at 370 ns after pulse.
Effect of plate Geometry: ROS
ICPM_2018
O3
O
1×1010
4×1014
High Rim
University of Michigan
Institute for Plasma Science & Engr.
Flat Rim
6×1010
4×1014
O3
O
3×1010
4×1014
Base Case
O3
O
Notes: Slightly higher O and O3 gas in flat rim but lower density in liquid. It can be due to higher residence time of RONS high rim plate

## Slide 14
Effect of plate Geometry: ROS
Flat Rim: Greater penetration of ambient gases enable production of ROS close to and liquid.
Density of OH is higher in the high rim due to “trapping” of evaporated water and results in higher H2O2 production.
OH + OH + M  H2O2 + M e + H2O  OH + H + e
HO2 + HO2  H2O2 + O2
ICPM_2018
2×1012
1×1012
6×1014
H2O2
HO2
OH
High Rim
University of Michigan
Institute for Plasma Science & Engr.
2×1014
3×1011
7×1012
H2O2
HO2
OH
Flat Rim
4-dec, cm-3
Notes: Check volave OH and OHL for the base case

## Slide 15
plate Geometry: after glow
10 ms after pulse, 3-decades, cm-3
High rim plate produces recirculation and vortices that traps, produces and enhances mixing resulting in higher O3 density.
Flat rim having He cross flow blows out RONS during afterglow.
ICPM_2018
5×1013
3×1012
5×1011
7×1012
High Rim
NO
O
OH
O3
University of Michigan
Institute for Plasma Science & Engr.
5×1013
3×1012
1×1011
2×1013
Flat Rim
NO
O
OH
O3
Notes: Creat gif for O3 50 ms duration

## Slide 16: ROS in Liquid
4×1014
3×1014
8×1012
7×1011
University of Michigan
Institute for Plasma Science & Engr.
Higher H2O2,aq and OHaq with high rim due to higher water vapor density in well.
O3,aq higher in high rim due to higher Oaq reacting with dissolved O2 even though O3(g) is lower .
O2- more uniformly distributed and higher density with flat rim due to IW across liquid, though high peak density in corner of high rim.
 Flat Rim
H2O2aq
OHaq
O3aq
O2−aq
2×1015
1×1015
2×1013
3×1012
80 ms after pulse
4-dec, cm-3
700 μm
ICPM_2018
 High Rim
8 mm
8 mm
Notes: Initially higher H2O2 in high-wall plate which can be from higher H2O vapor
@100ms slightly higher H2O2 in gas phase and liquid phase in high-well plate
O3 Initially higher in flush-well
Eventually higher in gas phase and liquid @ 100 ms in flush-well plate
Density of OH in both gas and liquid phase is similar
No2 Higher in gas and liquid phase in high well plate
Slightly higher O2- in high-well
***********
240 ms in high wall and 210 ms in flush well => 140 ms after pulse
NO2L: 9e9
1.5e10 high-wall

## Slide 17: RNS in Liquid
University of Michigan
Institute for Plasma Science & Engr.
Lower NOx with high rim in afterglow due to ambient dominated by He. However, higher ONOO− relates to higher OH. (NO2aq + OHaq  ONOOHaq).
NOx(g) accumulation above liquid with flat rim facilitates solvation.
NOaq should depend on O2 penetration to where N is large which is slightly higher in flat rim.
ICPM_2018
NOaq
ONOO−aq
NO2,aq
1×109
1×1011
3×109
700 μm
 High Rim
8 mm
5×1010
6×1010
2×1010
 Flat Rim
80 ms after pulse
4 dec, cm-3
8 mm
Notes: Slightly higher NO in v2 f17
Higher peroxinitrite and NO2
After glow:
NO2 slightly higher in gas and liquid in high rim
NO in gas equal in both plate
NOL slightly higher in flat rim

## Slide 18: AFTER GLOW RONS: HIGH VS. FLAT
University of Michigan
Institute for Plasma Science & Engr.
After glow starts at end of the pulse, 130 ms is plotted.
H2O2aq, O3 and OHaq higher in high rim after glow from a single pulse
NOx higher in flat rim.
ONOO− and O2 slightly higher in high rim.
ICPM_2018
 Flat Rim
 High Rim
Number particles (inv.)
H2O2aq
OHaq
O2−aq
O3aq
ONOO-aq
NO2aq
NOaq
H2O2aq
OHaq
O2−aq
O3aq
ONOO-aq
NO2aq
NOaq
Time After Plasma (s)
Time After Plasma (s)
Notes: Slightly higher NO in v2 f17
Higher peroxinitrite and NO2
After glow:
NO2 slightly higher in gas and liquid in high rim
NO in gas equal in both plate
NOL slightly higher in flat rim

## Slide 19: MULTIPLE PULSES: BASE CASE
University of Michigan
Institute for Plasma Science & Engr.
10 pulses, 1 kHz
Multiple pulses increases densities of longer lived species (H2O2 and O3) aided by recirculation from non-flux rim.
O and N are dominant inside the discharge gap.
H2O2 and OH formation follow water vapor.
ICPM_2018
5×1013, 2-dec
Animation Slide
3×1014, 3-dec
1×1012, 3-dec
Notes: Initially higher H2O2 in high-wall plate which can be from higher H2O vapor
@100ms slightly higher H2O2 in gas phase and liquid phase in high-well plate
O3 Initially higher in flush-well
Eventually higher in gas phase and liquid @ 100 ms in flush-well plate
Density of OH in both gas and liquid phase is similar
No2 Higher in gas and liquid phase in high well plate
Slightly higher O2- in high-well
***********
240 ms in high wall and 210 ms in flush well => 140 ms after pulse
NO2L: 9e9
1.5e10 high-wall

## Slide 20: MULTIPLE PULSES: High vs. flat
University of Michigan
Institute for Plasma Science & Engr.
10 KHz with 100 pulses, 3-dec cm-3
Higher H2O2 and OH and lower O3 with high rim as in a single pulse.
H2O2 and O3 production rate followed input energy in multiple pulses.
ICPM_2018
H2O2
5×1013
4×1014
OH
3×1013
8×1013
O3
4×1014
5×1013
Animation Slide
Notes: Frames outputed at 0.09 ms

## Slide 21: MULTIPLE PULSES: RONS
University of Michigan
Institute for Plasma Science & Engr.
10 KHz with 100 pulses, scaled density (cm-3, 3-dec)
Recirculation in high rim returns RNS into liquid surface increases their density.
ICPM_2018
NO2
2×1013
8×1013
NO
5×1013
HO2
NO2
NO
HO2
Animation Slide
2×1013
8×1013
5×1013
Notes: Frames outputed at 0.09 ms

## Slide 22: MULTIPLE PULSES: ROS in gas
University of Michigan
Institute for Plasma Science & Engr.
10 ms pulsed plasma treatment (100 pulses).
Density of vapor dependent species (H2O2, OH, H2 and HO2) is higher with high rim.
O is produced inside reactor independent of plate geometry.
ICPM_2018
O
H2O2
HO2
H2×10-1
OH
O3
Average density (cm-3)
Time (s)
Time (s)
O3
O
H2
H2O2
HO2
OH
O
High rim
Flat rim
Notes: 100 pulses
10 KHz

## Slide 23: MULTIPLE PULSES: ROS in LIQUID
University of Michigan
Institute for Plasma Science & Engr.
ROSaq is relatively higher in high rim.
Noticeable increase in HO2aq and H2aq with high rim.
High O3aq in High rim is due to higher Oaq (Oaq + O2aq  O3aq).
ICPM_2018
H2O2aq
HO2aq
H2aq
Oaq
OHaq
O2−aq
O3aq×10-1
H2O2aq
HO2aq
H2aq
Oaq
OHaq
O2−aq
O3aq×10-1
Time (s)
Time (s)
Number particles (inv.)
High rim
Flat rim
Notes: Initially higher H2O2 in high-wall plate which can be from higher H2O vapor
@100ms slightly higher H2O2 in gas phase and liquid phase in high-well plate
O3 Initially higher in flush-well
Eventually higher in gas phase and liquid @ 100 ms in flush-well plate
Density of OH in both gas and liquid phase is similar
No2 Higher in gas and liquid phase in high well plate
Slightly higher O2- in high-well
***********
240 ms in high wall and 210 ms in flush well => 140 ms after pulse
NO2L: 9e9
1.5e10 high-wall

## Slide 24: MULTIPLE PULSES: RNS in gas
University of Michigan
Institute for Plasma Science & Engr.
N production is inside reactor and independent of plate geometry.
RNS density is similar in both plate geometries.
NO2 density is slightly higher (3x) in high rim can be due to higher OH and HO2. HO2 + NO  OH + NO2
ICPM_2018
Average density (cm-3)
Time (s)
Time (s)
N
NO
NO2
N2O
N
NO
NO2
N2O
High rim
Flat rim
Notes: N2O depends on O => same
NO2 max in flash but vol_ave high in high
NO max in flash but vol_ave high in high
Higher H2O2,aq (1log) and OHaq in high rim plate due to higher water vapor
There is higher O3aq in high rim.
O2- is the same (H2OEL),
Noaq, NO2-, NO2 is the same
NO3- is higher (1-log) and HNO3L

## Slide 25: MULTIPLE PULSES: RNS in LIQUID
University of Michigan
Institute for Plasma Science & Engr.
ONOOH is the dominant RNS.
RNSaq is slightly higher in the high rim.
Solvated NxOy are the main source of RNS in liquid and then hydrolysis of acids: HNOx + H2O  NOx− + H+ .
ICPM_2018
Number particles (inv.)
Time (s)
ONOOHaq
NO2aq
HNO3aq
HNO2aq
NOaq
NO3−aq
ONOOHaq
NO2aq
HNO3aq
HNO2aq
NOaq
NO3−aq
Time (s)
High rim
Flat rim
Notes: Higher H2O2,aq (1log) and OHaq in high rim plate due to higher water vapor
There is higher O3aq in high rim.
O2- is the same (H2OEL),
Noaq, NO2-, NO2 is the same
NO3- is higher (1-log) and HNO3L

## Slide 26
CONCLUDING REMARKS
Height of the well plate changes gas mixture and dynamics of gas flow above liquid including water vapor.
Propagation of the IW out of the nozzle follows He gas channel and changes with the plate geometry:
Narrow IW distribution in flat rim due to penetration of ambient gas.
Volumetric IW propagation in high rim plate.
Recirculation and vortices during the after glow in high rim plate enhances gas mixing and residence time of RONS which enhances solvation of species.
High density He and water vapor in the high rim with minor diffused air results in higher OH and H2O2 production.
Multiple pulses (10 KHz) enhances production of RNSaq in high rim plate.
ICPM_2018
University of Michigan
Institute for Plasma Science & Engr.
Notes: 26